## Slide 1: Wave Propagation Explained

## Slide 2: Step1 – Finalize dimensions and resolutions
Calculate spatial/spectral plane lengths and resolution.
If using camera, then pixel and sensor size fixed.
Use sensor size x 2 (padded with zeros)
Then frequency resolution = 1/padded sensor size
Max frequency (w/o aliasing) = 1/pixel size /2
Max cos angle (w/o aliasing) = max freq x wavelength
IMPORTANT: set measurement standard for example mm.

## Slide 3: Step 2 – (Optional)
Evaluate max frequencies based on setup
As z increases, max angle reduces.
Spatial frequencies reaching the next plane reduce.
As aperture size increase, more frequencies reach the next plane and there is less diffraction.

## Slide 4: Step 3 – Bandlimit wave transfer function
The transfer function H(f) behaves like a chirp function
Use local spatial frequency (derivate of the phase) to find the sampling (Nyquist rate) required for H(f)
As this sampling is fixed based on step 1, evaluate max frequency possible w/o aliasing using this this sampling rate in the frequency domain (1/ size of the spatial support).
Use a mask to zero out (discard) exceeding frequency components.

## Slide 5: Step 4 – Finally
Multiply the bandlimited transfer function with the spectrum at the input plane to find the spectrum at the output plane.
Take the inverse Fourier and discard the padding (added in the first step) to obtain the wave in the output plane.